## Slide 1: Networks of Queues
CSCE 654
Computer Communication Networks
Dr. Scott Graham
Department of Electrical and Computer Engineering
Air Force Institute of Technology
(Material from Maj Tom Dube, Maj Ryan Thomas, Maj Scott R. Graham, Dr. Barry Mullins & Dr. Scott Midkiff is gratefully acknowledged)

## Slide 2: Outline
Motivation and analytical difficulties
Open versus closed networks of queue
Product form solutions
  Jackson’s Theorem
Kleinrock Independence Approximation
Burke’s Theorem
Closed networks of queues

## Slide 3: Reading
T. G. Robertazzi, Computer Networks and Systems, 3rd edition, Sections 3.1-3.2.

## Slide 4: Networks of Queues
Single queues might represent a single transmission line, channel, connection, session, etc.
Data networks consist of many transmission lines or channels
We need to model networks as a network of interacting queues, not as a single queue

## Slide 5: Networks of Queues: Simple Example (1)
1
2
a
b
a
b
c
Simple network with two transmission lines (1 and 2) and three nodes (a, b, and c)
  Arrivals can occur at nodes a and b
  Departures can occur at nodes b and c

## Slide 6: Networks of Queues: Simple Example (2)
Queuing model
  Each link is a queue in the network
  Need to know routing probabilities
a
b
1
2
a
b
c
1
2
How many packets from node a depart the system at node b?

## Slide 7: Networks of Queues: Another Example
Arriving traffic at each queue (transmission line) may include:
  Internal traffic that has departed from one or more other queues
  External traffic that is entering the network
1
2
3
4
5
a
b
c
d

## Slide 8: Analytical Difficulties: Part 1 (1)
Consider two tandem transmission lines (queues) with equal capacity (service rates)
  Arrivals to the system are Poisson
  Packets are of equal length, i.e. fixed service times
With these assumptions, the first queue is an M/D/1 queue
  P-K formula gives average packet delay
m
l
m
M/D/1

## Slide 9: Analytical Difficulties: Part 1 (2)
What about the second queue?
  Interarrival times, tn, are not Poisson
m
l
m
M/D/1
M/D/1
For Poisson arrivals:

## Slide 10: Analytical Difficulties: Part 1 (3)
Consider the second queue
  Interarrival time, tn, the time between arrivals of packets n and n+1
  Service time for packet n, sn
    Remember that n is only equal to sn under a heavy load (r1)
Note that sn £ tn, so packet n+1 never queues
  N < 1 NQ = 0 T = 1/m W = 0
Second queue is clearly not M/D/1
n
sn
n+1
tn

## Slide 11: Analytical Difficulties: Part 2 (1)
Consider what should be a “cleaner” version of the tandem queues -- Poisson arrivals and exponential packet lengths (service times)
  First queue is M/M/1
  Second queue is not M/M/1 since interarrival times at the second queue are correlated with packet service times
m
l
m
M/M/1

## Slide 12: Analytical Difficulties: Part 2 (2)
At the second queue
  Interarrival time between packet n and n+1 is greater than or equal to the transmission time for packet n+1, i.e., tn ³ sn+1.
  A long packet that arrives at the second queue is more likely to find fewer customers in queue
Arrivals to queue 1
Arrivals to queue 2
Queue 1
Queue 2
n+1
n
n
n+1
sn
sn+1
tn
n-1

## Slide 13: Product Form Solutions
Let the state of an M-queue network be defined by a vector
  (n1, n2,…, nM)
  ni is the number of “customers” in queue or in service at queue i.
Product form solutions
  Joint state probabilities expressed as the product of probabilities associated with the individual queues
  P(n1, n2,…, nM) = P(n1) P(n2) … P(nM)
Queues act as though they are independent
  At a specific point in time, the number of customers in one queue is independent of the number of customers in another queue
  Not independent at two different close times

## Slide 14: Open vs Closed Networks
Open networks of queues,
  Customers arrive and depart from the network
    For example, packets in a network
Closed networks of queues
  A fixed number of customers circulate within the network
    For example, processing jobs in a computing system

## Slide 15: Closed Networks of Queues
CPU
m1
m2
I/O
p
1-p
Fixed number of jobs circulate between queues
  Job returns to CPU with probability p
  Job require I/O with probability 1-p
We’ll discuss closed networks later

## Slide 16: Notation for Open Networks of Queues
: total mean arrival rate to the network
i: mean service rate of i-th server
rsj: probability that a customer arriving from the source will be routed to queue j
rjd: probability that a customer departing from queue j will be routed to the destination (and depart the system)
rjk: probability that a customer departing from queue j will be routed to queue k

## Slide 17: Open Networks of Queues
rs1
rs3
rs2
r11
r33
r21
r12
r32
r3d
r2d
r1d
l
l
source
destination
m1
m3
m2
r22
r23
Customers enter and leave the system, but take a path through zero or more queues
Our initial focus
Q1
Q2
Q3

## Slide 18: Example: Tandem Queues
rs1 = 1
r12 = 1
r23 = 1
r3d = 1
l
Q1
Q2
Q3
S
D
1
2
3

## Slide 19: Example: Multi-Stage Network
Stage 1
Stage 2
Stage 3
D
l
rjk > 0 only between adjacent stages
S

## Slide 20: Example: General Topology
D
l
S

## Slide 21: Average Throughput
Let i be the average throughput through queue i
  Mean rate of entering (leaving) a particular queuing system
Traffic equations …

## Slide 22: In-Class Exercise 1
Find the average throughput, 1 and 2, for each queue in the following network of queues (as a function of ).
1/4
1/2
l
Q1
Q2

## Slide 23: In-Class Exercise 1: Solution
Find the average throughput, 1 and 2, for each queue in the following network of queues (as a function of ).
Solving yields …

## Slide 24: State Description of the System
The state of a system with M queues can be defined as an M-element vector, where ni is the number of customers in the i-th queuing system (in queue and in service)
Our goal is to find the pmf of n

## Slide 25: Global Balance Equations (1)
Arrival to any queue
from outside
Departure from any
queue
Global balance equations …
  Rate of arrival from any queue must equal rate of departure to any queue
Let (n) be the probability of being in state n
What is the rate of leaving state n?

## Slide 26: Notation: The i-th Unit Vector
i-th position

## Slide 27: Global Balance Equations (2)
What is the rate of entering state n?
External arrival
External departure
Movement from j to i

## Slide 28: Global Balance Equations (3)
=
Rate in must equal rate out …

## Slide 29: Solving for Product Form Solution (1)
Substituting traffic equations into global balance equation…

## Slide 30: Solving for Product Form Solution (2)

## Slide 31: Local Balance Equations
Local balance equations are generalizations of the balance equations from the M/M/1 queue
Local balance equations, plus global balance equations and traffic equations, provide product form solution

## Slide 32: Solving for Product Form Solution (3)
Traffic flow into network related to flow out of network (in equilibrium).

## Slide 33: Solving for Product Form Solution (4)
Taken further…
Recursing until ith element is zeroed out yields this equation.
Probability that ith queue is empty.

## Slide 34: Product Form Solution
Joint pmf
Network behaves as if all queues were statistically independent!
Look familiar?

## Slide 35: In-Class Exercise 2
In the network of queues from the previous exercise, assume Poisson arrivals at an average rate of 1,000 packets/s and average service times at each queue of 0.2 ms.
What is the probability of no packets being in the system?
1/4
1/2
l
Q1
Q2

## Slide 36: In-Class Exercise 2: Solution
What is the probability of no packets being in the system?

## Slide 37: Marginal pmf
Due to the product form, the marginal pmf of ni customers in the i-th queuing system is …
Borrowing from analysis of M/M/1 queue …

## Slide 38: Customers and Delay in the Network
Results for the full network …
Fraction of packets at queue i
Delay at queue i

## Slide 39: In-Class Exercise 3
For the network in the two previous exercises, what is …
  (a) the average number of packets in the network?
  (b) the average delay through the network?
1/4
1/2
l
Q1
Q2

## Slide 40: In-Class Exercise 3: Solutions
What is …
(a) the average number of packets in the network?
(b) the average delay through the network?

## Slide 41: Jackson’s Theorem: Overview
Jackson’s Theorem was the first to show the product form solution for networks of queues
Jackson’s Theorem indicates that the average number of customers in the system can be derived by treating each queue as an M/M/1 queue
  Correlation between transmission times and interarrival times eliminated
  Randomization divides traffic among different routes

## Slide 42: Jackson’s Theorem: Assumptions (1)
Poisson arrivals to the system and exponential service times
  Note that arrivals to individual queues will, in general, not be Poisson
Independence of interarrival times and packet lengths
Network
lm
l1
l2
l3
l4
l5
l6
l7
...

## Slide 43: Jackson’s Theorem: Assumptions (2)
Stream splitting is randomized using probabilities rij which apply to all packets departing from queue i
  Different streams may not have different routing probabilities
  Jackson’s Theorem may be extended to account for different classes of customers

## Slide 44: Jackson’s Theorem (1)
The state of the system is a vector,
Jackson’s Theorem: Assuming rj < 1, j = 1,..., M, then for all n1, n2,..., nM,
where and

## Slide 45: Jackson’s Theorem (2)
Jackson’s Theorem states:
  The number of customers in each queue in the system is distributed as if each queue is M/M/1
  The number of customers in each queue is independent of the number in other queues
  The total arrival process at each queue need not be Poisson!

## Slide 46: Approximate Models
Product forms do not apply to many networks of interest, so approximations and/or simulation are often necessary
Independence between arrival rate and service times is lost at the second of two tandem queues




## Slide 47: Approximate Models
The Kleinrock independence approximation (KIA) provides an approach to analyze delay in networks carrying multiple packet streams
  Based on the assumption that merging packet streams from several sources “restores” the independence of interarrival times and packet lengths
  Allows networks to be analyzed as multiple queues, e.g., as multiple M/M/1 or M/G/1 queues

+
...


## Slide 48: Approximate Models
Good approximation for systems with …
  Poisson stream arrivals at the entry points
  Packet lengths that are approximately exponentially distributed
  High degree of network connectivity
  Moderate-to-heavy traffic
System can be analyzed assuming that each transmission line is treated as an M/M/1 queue
Similar results can be derived for non-exponential packet lengths using the P-K formula for the M/G/1 queue model

## Slide 49: KIA: Network Model (1)
Consider a set of packet streams
  Packets from each stream enter the network at a source node, follow a fixed and unique path, and depart from the network at their destination
  Let xS be the arrival rate (in packets/second) for stream S
Each link in the network carries packets from all streams whose path includes that link
  Arrival rate for link (i,j) connecting nodes i and j

## Slide 50: KIA: Network Model (2)
x1
x2
x3
x4
1
2
3
4
l23=x2+x3
l34=x4
l41=x3
l12=x1+x2+x3

## Slide 51: KIA: Network Model (3)
This model is appropriate for virtual circuit networks
  Each stream represents a separate virtual circuit
  Packets follow a fixed path through the network

## Slide 52: KIA: Network Model (4)
Can be adapted to model datagram networks
  Packets from the same stream may take different paths through the network
  Let fij(s) be the fraction of stream s packets that go over link (i,j)
  Link arrival rate is

## Slide 53: Analysis Using KIA (1)
Recall that for link (i, j),
Let 1/mij be the average packet transmission time for link (i, j)
Using the M/M/1 model, the average number of packets in queue or in service at link (i, j), Nij is

## Slide 54: Analysis Using KIA (2)
The average number of customers in the system is obtained by summing the number at each link …

## Slide 55: Analysis Using KIA (3)
Let g be the total arrival rate for the system, where xS is the packet arrival rate for stream S
x1
x2
x3
x4
x5

## Slide 56: Analysis Using KIA (4)
Using Little’s Law, the average delay per packet in the system is

## Slide 57: Analysis Using KIA (5)
This can be rewritten as where Tij is the delay at link (i, j), and aij is the fraction of the system traffic going over link (i, j)

## Slide 58: Analysis Using KIA (6)
The average delay per packet can be adjusted to account for processing and propagation delay dij at link (i, j)
  The average processing and propagation delay due to link (i, j) is
  The modified delay is

## Slide 59: Analysis Using KIA (7)
The average delay per packet of a stream following path p:
  Wij is the waiting time at link (i, j)
  rij is the utilization of link (i, j), rij = lij /mij

## Slide 60: KIA Application: Delay (1)
Consider a 4-node network with 8 links
  There are 4 connections, each with a pair links in the forward and reverse directions
There are 10 packet streams with Poisson arrivals
Packet lengths are exponentially distributed

## Slide 61: KIA Application: Delay (2)
A
C
D
B
2
1
3
4
F
F
F
F
R
R
R
R

## Slide 62: KIA Application: Delay (3)

## Slide 63: KIA Application: Delay (4)

## Slide 64: KIA Application: Delay (5)
The greatest contributor to delay is the delay on link 2 because of the relatively high arrival rate
Approaches to reducing delay …
  Routing: Reduce the arrival rate at link 2 by more evenly distributing traffic (cannot be done here)
  Capacity Assignment: Decrease transmission times on heavily used links
  Topology: Change the network topology to allow alternate paths that routing can use to distribute traffic
Consider reassigning capacity

## Slide 65: KIA Application: Delay (6)
Increase Link 2 (2F and 2R) capacity by 50% from 10 to 15 units

## Slide 66: KIA Application: Delay (7)
With Link 2 capacity 1.5 times greater

## Slide 67: Burke’s Theorem (1)
Because of the property of time reversibility, “forward” and “reversed” systems are statistically indistinguishable
Burke’s Theorem: Consider an M/M/1, M/M/m, or M/M/¥ queue in steady state with arrival rate l
  a) The departure process is Poisson with rate l
  b) At each time t, the number of customers in the system is independent of the sequence of departure times prior to t

## Slide 68: Burke’s Theorem (2)
Forward Chain Arrivals, A(t) Departures, D(t)
Reverse Chain Departures, D*(t) Arrivals, A*(t)

## Slide 69: Burke’s Theorem: Comments (1)
Part b of Burke’s Theorem is, perhaps, not intuitive
  If we have just observed a burst of departures, we might expect that there are presently a large number of customers in the system
  However, the number of customers in the system is independent of the burst of prior departures
  Note that Burke’s Theorem does not address the number of customers in the system prior to the burst of departures

## Slide 70: Burke’s Theorem: Comments (2)
Burke’s Theorem holds for general acyclic networks of queues with Poisson arrivals and independent, exponentially distributed service times

## Slide 71: Acyclic Networks (1)
Queue j is a downstream neighbor of queue i if there is a positive probability that a departure from queue i will next enter queue j
Queue k is downstream of queue i if there is a sequence of queues from i to k where each of the queues in the sequence is a downstream neighbor of its predecessor
A network is acyclic if there are no two queues i and k s.t. i is downstream of k and k is downstream of i

## Slide 72: Acyclic Networks (2)
A counter-example — a cyclic network …
  k is downstream of I
  i is downstream of k
i
j
k

## Slide 73: Burke’s Theorem: Application (1)
Consider two tandem transmission lines modeled as M/M/1 queues
  Assume that a given packet’s transmission times on the first and second links are independent (as though packets are “resized” at each link)
  Arrival rate is l
  Service rates are m1 and m2 at the first and second queues, respectively
m1
l
m2

## Slide 74: Burke’s Theorem: Application (2)
Utilizations: r1 = l/m1 < 1, r2 = l/m2 < 1
The first queue is clearly M/M/1, so
Arrivals to the second queue are Poisson with rate l (due to Burke’s Theorem) and service times are independent from arrivals (by assumption), so the second queue is also M/M/1

## Slide 75: Burke’s Theorem: Application (3)
From Part b of Burke’s Theorem:
  The number of customers presently in queue 1 is independent of prior departures from queue 1 (and thus prior arrivals to queue 2)
  The number of customers presently in queue 1 is independent of the number of customers presently in queue 2
Given this independence,

## Slide 76: Routing in a Network of Queues (1)
Three factors that affect network performance …
  Routing
  Capacity assignment
  Topology
In the KIA analysis example, we examined capacity assignment
  Capacity assignment and topology design will be covered more later in the class
Let’s take a (simple) look at routing using a network of queues

## Slide 77: Routing in a Network of Queues (2)
Static routing
  Routes are fixed, i.e., selection is predetermined
    Virtual circuit routing — based on source and destination of virtual circuit
    Datagram routing — based on destination of datagram
  Routing probabilities are fixed
Dynamic routing
  Goal is to adjust routing to respond to changes in load
    Take advantage of short-term variability
    Cope with long-term non-stationary traffic
  Routing probabilities are state-dependent

## Slide 78: Static Routing (1)
Consider the very simple “network”
  Packets arrive with rate 
  Service rates are 1 and 2 on links 1 and 2, respectively
  Packets is routed on link 1 (with probability p) or on link 2 (with probability 1-p) … what value of p is best?
S
D
1
2

1
2
p
1-p

## Slide 79: Static Routing (2)
Want to minimize delay …
S
D
1
2

1
2
p
1-p

## Slide 80: Static Routing (2)
Would like to choose p = p* such that T is minimized
In general, delay T is a complex function of the routing probabilities and numerical methods are needed to find the optimal set
0
p*
1
T

## Slide 81: In-Class Exercise 4
Suppose you observe two queues, 1 and 2, and estimate that E[n1] < E[n2], i.e., that queue 1 is shorter. Should you chose to submit a job (route a packet) to queue 1 or to queue 2?
Trick question …
Little’s Law tells us that E[T] = E[n]/.
Knowing just E[n] does not provide enough information to determine delay. The shorter line is faster only if the arrival rate (or departure rate) is sufficiently high.

## Slide 82: Closed Networks of Queues
CPU
m1
m2
I/O
p
1-p

## Slide 83: Model of a Closed Network of Queues
Closed networks of queues can be used to model different types of systems
  In reality, system is open
Number of customers in the system at any time is a fixed value N

## Slide 84: Applications
Finite population models (M/M/s/s/K)
  Each of K users can have at most 1 call active at a time
  Maximum number of calls is K
Systems under heavy loads
  Multi-stage packet switches with a finite number of packets allowed in, and a new packet is always ready to enter when one leaves
Window-based flow control
  Maximum number of packets in transit at any time

## Slide 85: Traffic Equations
Traffic equations for a closed network …
Like traffic equation for open networks, except no term for sources (rsi)
Unlike open networks, these do not have a unique solution

## Slide 86: Global Balance Equations
=
Net flow out of state n
Net flow out to state n
(customers change from queue j to i)

## Slide 87: Closed Network Product Form Solution
G(M,N) is a normalization constant

## Slide 88: Closed Network Example (1)
Computer system allows two active jobs at any given time
Each job requires CPU and I/O processing
CPU
m1
m2
I/O
p
1-p

## Slide 89: Closed Network Example (2)
When a job leaves the CPU, there are two possibilities …
  The job finishes and is instantly replaced by another job (with probability p)
  The job requires I/O, then more CPU (with probability 1–p)
CPU
m1
m2
I/O
p
1-p

## Slide 90: In-Class Exercise 5
Let the system state (n1, n2) indicate that there are n1 jobs in the CPU and n2 jobs in I/O.
  Enumerate the possible states.
  List the traffic equations (two equations).
CPU
m1
m2
I/O
p
1-p

## Slide 91: In-Class Exercise 5: Solution
Let the system state (n1, n2) indicate that there are n1 jobs in the CPU and n2 jobs in I/O.
  Enumerate the possible states.
  List the traffic equations (two equations).
Three states: (2,0), (1,1), (0,2)

## Slide 92: Closed Network Example (3)
Product form solution for the example …

## Slide 93: Closed Network Example (4)
Normalization factor …
State (1,1)
State (0,2)
State (2,0)

## Slide 94: Comments on Normalization Factor
This method for finding the normalization constant is impractical for a large system
Algorithms for numerical computation can be used to determine G(M,N)
  For example, the convolution algorithm for closed networks

## Slide 95: Closed Network Example (5)
Steady-state probability for state (2,0) …

## Slide 96: In-Class Exercise 6
Determine the steady-state probabilities for states (0,2) and (1,1) — as a function of service rates and routing probabilities.
Equations, but in terms of ’s and G(2,2) …

## Slide 97: In-Class Exercise 6 (Solutions 1)
Recall that …
Normalization constant …

## Slide 98: In-Class Exercise 6 (Solutions 2)
Steady-state probability for state (0, 2) …

## Slide 99: In-Class Exercise 6 (Solutions 3)
Steady-state probability for state (1, 1) …

## Slide 100: Utilization
Utilization i is the proportion of time that server i is busy
  Let i’ be the actual arrival rate to queue i
  The utilization of queue i is …
Other methods are available
  For the example, queue i is busy if it is occupied by ni > 0 jobs …

## Slide 101: In-Class Exercise 7
Use the same example network. Let …
  1 = 4 jobs/s
  2 = 1 job/s
  p = 1/3
(a) Calculate the state probabilities.
(b) Calculate the utilization at each queue.
(c) Calculate the average number of customers in each queuing system.
(d) Calculate the average delay through each queuing system.

## Slide 102: In-Class Exercise 7: Solution (a-1)
(a) Calculate the state probabilities.

## Slide 103: In-Class Exercise 7: Solution (a-2)
(a) Continued …

## Slide 104: In-Class Exercise 7: Solution (a-3)
(a) Continued …
Or …
([1,1]) = 1 - ([2,0]) - ([0,2]) = 1 - .66 - .093 = .247

## Slide 105: In-Class Exercise 7: Solution (b)
(b) Calculate the utilization at each queue.

## Slide 106: In-Class Exercise 7: Solution (c)
(c) Calculate the average number of customers in each queuing system.

## Slide 107: In-Class Exercise 7: Solution (d)
(d) Calculate the average delay through each queuing system.

## Slide 108: You should now be able to … (1)
Explain why networks of queues are more difficult to analyze than single queues
Define closed and open networks of queues
Use product form solutions and Jackson’s Theorem to analyze an open network of queues in terms of delay, number of customers, and utilization
Apply the Kleinrock independence approximation to analyze a network of queues

## Slide 109: You should now be able to … (2)
Calculate state probabilities, average number in system and average delay for closed networks of queues