## Slide 1: Motivation
CSCE 654
Computer Communication Networks
Dr. Scott Graham
Department of Electrical and Computer Engineering
Air Force Institute of Technology
(Material from Dr. Barry Mullins & Dr. Scott Midkiff is gratefully acknowledged)

## Slide 2: Outline
Traditional management, design, and performance (or “how not to manage a network”)
Performance, design, and management
Performance analysis methods
Examples

## Slide 3: References
R. Jain, The Art of Computer Systems Performance Analysis: Techniques for Experimental Design, Measurement, Simulation, and Modeling, John Wiley and Sons, 1991.
M. H. MacDougall, Simulating Computer Systems: Techniques and Tools, MIT Press, 1987.
D. W. Petr, Course Notes, The University of Kansas, 1999.
W. Stallings, High Speed Networks: TCP/IP and ATM Design Principles, Prentice-Hall, 1998.

## Slide 4: “Algorithm” for Network Operation (1)
Consider the operation of a LAN for client/server intranet applications
Operation “algorithm”
  1. // deploy LAN based on current technology and
  2. // constrained by budget;
  3. do {
  4. while (no complaints) {
  5. surf the web
  6. }
  7. surf to a trade magazine site;
  8. buy latest technology constrained by budget;
  9. deploy latest technology;
  10. if (key users not happy) {
  11. increase budget and go to 5
  12. }
  13. } while (still employed)

## Slide 5: “Algorithm” for Network Operation (2)
Even in this ad hoc, far-from-optimal approach to network operation, there is a connection between management, evaluation, and design
  Management: Note the lack of user complaints
  Evaluation: Ascertain the reason for the whining
  Design: Buy some stuff and make it work
Problems
  Likely to spend too much
  Excessive periods of poor performance
  Problem may not be fixed
  Responding to perception, not reality

## Slide 6: Performance, Design, and Management
Performance
Evaluation/Analysis
Network
Design
Network
Management

## Slide 7: Performance Evaluation
We can predict the behavior of networks “using pencil, paper, the poetry of mathematics and the number-crunching ability of computers.” (T. Robertazzi)
Tools
  Probability and queuing theory
  Traffic models
  Simulation

## Slide 8: Design
“A network design is a blueprint for building a network. The designer has to create the structure of the network [and] decide how to allocate resources and spend money.” (R. Cahn)
Tools
  Capacity assignment techniques
  Graph theory
  Computer-aided design tools

## Slide 9: Management
“… our only real option is to use the network to manage the network. This means we need a protocol that allows us to read, and possibly write, various pieces of state information on different nodes.” (L. Peterson & B. Davie)
Tools
  Management protocols, e.g., SNMP
  Management tools
  Experiments

## Slide 10: Network Models
What are we modeling?
Networks (broadly defined) generally fall into one of three categories
  Resource sharing networks
  Process networks
  Switching networks

## Slide 11: Resource Sharing Networks (1)
Time-shared computer (Programs : CPU/Disk/IO)
Statistical multiplexer/concentrator
Packet-based (Packets : Links)
Channel-based (Calls : Channels)
Multiple-Access and random access networks (Packets : Shared Medium)
Shared Resources
User 1
User N
…

## Slide 12: Resource Sharing Networks (2)
Performance measures
  Waiting time
  Blocking probability
Questions
  What is the relationship between the number of users, the pattern of usage, the amount of resources, and the performance?
  Are resources utilized fairly (or appropriately) by the users?

## Slide 13: Process Networks (1)
Process 1
Process 2
Process 3
Input 1
Input 2
Input 3
Input 4
Output
Multi-stage switch
Distributed simulation system
Manufacturing process

## Slide 14: Process Networks (2)
Performance measures
  Time to complete (delay)
  Throughput (completions per unit time)
Questions
  How is performance affected by different use patterns?
  Which processes are the “bottlenecks” that constrain performance?
  Are different inputs treated fairly with respect to performance?

## Slide 15: Switching Networks (1)
Telephone network (Phones : Circuit Switches)
Telephone signaling network (Switches : STPs)
X.25 packet network (Computers : Packet Switches)
Internet (Computers : Routers)
Endpoint
Endpoint
Endpoint
Switch
Switch
Switch
Switch
Endpoint

## Slide 16: Switching Networks (2)
Performance measures
  Delay (endpoint to endpoint)
  Throughput
  Utilization
  Blocking probability
  Losses
Questions
  What is the best topology?
  How do we route?
  How do we guarantee Quality of Service?

## Slide 17: Performance Analysis (1)
Why?
  Bottleneck or capacity analysis
  Sensitivity of performance to parameters
  Detecting problem areas to guide system tuning
  Configuration planning and trade-offs
  Benchmarking
When?
  Architecture/system design
  Detailed design and implementation
  Operation

## Slide 18: Performance Analysis (2)
How?
  Analytical models, e.g., queuing models with closed form or numerical solutions
  Simulation experiments, e.g., discrete-event simulation with statistical results
  Empirical measurements, e.g., instrumented code and network monitoring

## Slide 19: Systematic Approach (1)
State goals of the study and define the system
  Delineate system boundaries
  Goals will determine appropriate boundaries
List services (functions) and outcomes of services
Select metrics
  Examples: throughput, latency, availability, etc.
List parameters that affect performance
  System parameters
  Workload parameters
Select factors to study
  Factors are parameters that will be varied
  Other parameters will remain fixed
Select evaluation technique
  Analytical
  Simulation
  Measurement

## Slide 20: Systematic Approach (2)
Select workload, or list of service requests
  Probability distributions for analytical study
  Trace or distribution for simulation study
  Scripts for measurements
Design experiments
  Phase 1: Large number of factors, few values
  Phase 2: Small number of factors, many values
Analyze and interpret results
  Results are random
  Statistical techniques needed to compare results
Present results
  Graphical techniques
  Refinement and iteration may be needed

## Slide 21: Evaluation Techniques
Criterion Analytical Simulation Measurement
Stage Any Any Post-prototype
Time required Small Medium Varies
Accuracy Low Moderate Varies
Trade-off Easy Moderate Difficult Evaluation
Cost Low Medium High
“Saleability” Low Medium High
þ Use of multiple techniques allows validation

## Slide 22: Example: ISP (1)
An ISP provides circuit-switched access (phone lines) to the Internet
How many lines (maximum simultaneous active connections) should be supported?
  Customer satisfaction  Large number of lines to reduce probability of blocking (busy)
  Operating costs  Small number of lines to reduce equipment, line, maintenance, and power costs
When should new lines be provisioned?
  What are the tolerances of customer satisfaction and operating costs?

## Slide 23: Example: ISP (2)
What policies should be in place to maximize profit?
  Charge a flat fee or charge for connect time?
  Limit sessions to X hours?
  Automatically disconnect inactive users after Y minutes?
  Differentiate service based on price?
These questions define the goals and the system for a performance study
  Management information needed for the study
  Results of study can be applied to optimize design of modem pool (and policies)

## Slide 24: Example: ISP (3)
Performance
Evaluation
Network
Design
Network
Management
Optimized modem pool and polices
Effect of number of lines and polices on performance
Workload characteristics and current performance

## Slide 25: Example: ISP (3)
Note that this is a “resource sharing network”
  Users must share a limited number of lines
  Number of users exceeds the number of lines
  If number of active users equals the number of lines, further use attempts by other users will be blocked
Shared Resources
User 1
User N
…

## Slide 26: Example: ISP (4)
Metrics
  Blocking probability
  Wait time (until a line is free)
System parameters
  Number of lines
Workload parameters
  Number of calls (arrival or attempt rate)
  Length of call (holding or service time)
  Time until retry attempt if blocked
Factors to vary for the study
  Number of lines
  Number of users (attempt rate)

## Slide 27: Example: ISP (5)
Evaluation techniques
  Analytical (Erlang model)
  Measurement of specific configuration(s) to validate analytical results
Select workloads
  Assumptions
    Holding time
    Probability of an attempt from a user
    Retry characteristics
  Assumptions can be developed by monitoring use patterns
    Requires network management (monitoring)

## Slide 28: Example: ISP (6)
Design and conduct experiments
  Easy for analytical study
  More difficult for measurements
Analyze and interpret results
  Again, easy for analytical study and more difficult for measurements
Present results
  Validation of analytical results using measurements increases confidence in results

## Slide 29: Studying the Virginia Tech Modem Pool
Traffic assumptions
  Measurements made on the Virginia Tech modem pool
Simulation using OPNET Modeler™
Problem
  Look at call blocking probability
  Analyze the impact of increasing the number of modems versus imposing a rule to drop all calls after X hours
D. Novak, D. Rowland, M. Stepanek, D. Watkins and L. A. DaSilva, "Modem Pool Simulation and Performance Analysis," in the proceedings of 2000 SCS Symposium on Performance Evaluation of Computer and Telecommunication Systems (SPECTS'2K), July 16-20, 2000, Vancouver, Canada, pp.88-95.

## Slide 30: Simulation Results

## Slide 31: Validation versus Verification
Verification (usually easy to do)
  Is the model properly constructed?
  Analytical model: “Is the math right?”
  Simulation model: “Is the model properly coded?”
Validation (often hard to do)
  Does the model accurately represent the behavior of the system of interest?
  Analytical model: “Is the model ‘correct’?”
  Simulation model: “Is this an accurate simulation for the questions of interest?”

## Slide 32: Example: Backbone Service (1)
A carrier provides backbone services to companies and lower-tier ISPs
  Internet access to companies and ISPs
  Virtual private network (VPN) service for corporate networks
Backbone Network
ISP
X
Y
Y
X
Internet

## Slide 33: Example: Backbone Service (2)
This is a “switching network”
  Customer networks are endpoints
  IP routers in the backbone are switches
Backbone network defines system boundary
ISP
X
Y
Y
X
Internet
Backbone

## Slide 34: Example: Backbone Service (3)
Throughput objectives – relatively simple
  Maximize network throughput given a maximum cost constraint
  Minimize cost given a minimum throughput constraint
Throughput factors
  Network topology
  Link capacity
  Router capacity
  Routing algorithm (efficiency)
  Workload (characteristics of traffic leaving customer networks)

## Slide 35: Example: Backbone Service (4)
Network management
  Identify problems
    Bottlenecks
    Routing problems
    Misbehaved customer networks
    Link and router failures
  Monitor traffic to model workload
Performance evaluation
  Study effects of network design changes
  Study effects of workload changes
  Identify bottlenecks
  Proactive planning for network growth

## Slide 36: Example: Backbone Service (5)
Network design
  Adjust link capacity, router capacity, and topology
  Optimize routing
Performance
Evaluation
Network
Design
Network
Management

## Slide 37: Example: Backbone Service (6)
Quality of service (QoS) or service level agreement (SLA) objectives – relatively complex
  Guaranteed throughput over some period of time
  Maximum delay
  Maximum delay variation
  Availability
Customer network issues imply need for network management
  Monitoring service level agreements
  Policing traffic

## Slide 38: Example: Backbone Service (7)
Backbone network issues
  To what set of SLAs can a carrier commit with a given set of network resources?
  How to optimize the network for a given set of SLAs?
  How much to charge for a given SLA?
  How to optimize revenue?
Management, performance evaluation, and design must be considered to optimize the network operation (and revenues)

## Slide 39: Example: Packet Switch Design (1)
An equipment vendor is designing a high-performance Layer 3 IP switch
…
Switching Fabric
Control
…
Inputs
Outputs

## Slide 40: Which of the network models fits?
Resource sharing networks
Process networks
Switching networks
…
Switching Fabric
Control
…
Inputs
Outputs

## Slide 41: Example: Packet Switch Design (2)
If implemented as a multi-stage switch
  System is a “process network”
Input
Input
Process
Input
Input
Process
Process
Process
Output
Output
Output
Output

## Slide 42: Example: Packet Switch Design (3)
If implemented as a TDMA bus
  System is a “resource sharing network”
Input
Input
Input
Input
Output
Output
Output
Output
Bus

## Slide 43: Example: Packet Switch Design (4)
There are many performance issues
  Aggregate and per port throughput
  Input-to-output delay
  Introduced delay variation (jitter)
  Blocking probability
  Packet loss due to queue overflow
  Reliability
  Fairness

## Slide 44: Example: Packet Switch Design (5)
Without an operational system to manage (monitor), the process involves just …
  Design
  Performance and cost evaluation (predictive)
System
Design
Performance Evaluation

## Slide 45: Example: MAC Protocol Design (1)
A researcher is developing a new multiaccess control protocol for a wireless ad hoc network
This is a “resource sharing network”
  Stations (e.g., A, B, and C) are the users
  Radio spectrum is the shared resource (medium)
Will be analyzed in excruciating detail using queuing theory in week 4
A
B
C

## Slide 46: Example: MAC Protocol Design (2)
There are many performance issues
  System throughput
  Packet delay
  Allocation of system throughput (fairness)
  Channel utilization
  Probability of collision
There are a number of factors affecting performance
  Offered traffic
  Number of stations (and placement)
  Channel characteristics
  Protocol operation

## Slide 47: Example: MAC Protocol Design (3)
Many design issues …
Spectrum (shared resource) sharing
  Circuit-switched schemes
    Frequency division multiple access (FDMA)
    Time division multiple access (TDMA)
    Code division multiple access (CDMA)
  Packet-switched time division multiplexed (TDM) schemes
    Reservation-based TDM schemes, e.g., packet reservation multiple access (PRMA)
    Contention-based TDM schemes, e.g., carrier sense multiple access (CSMA)

## Slide 48: Example: MAC Protocol Design (4)
Optimizing or “tuning” a basic scheme
  How many channels to allocate in a circuit-switched system?
  Effectiveness of collision avoidance schemes in a contention-based system?
  Efficiency of scheduling schemes in a reservation-based system?
Specifying system performance
  How many users?
  How much capacity per user?
  Physical layer requirements?

## Slide 49: You should now be able to … (1)
Cite motivation for …
  Performance evaluation
  Systematic design techniques
  Network management
Describe three models of networked systems and cite examples
  Resource sharing networks
  Process networks
  Switching networks

## Slide 50: You should now be able to … (2)
List the three types of performance study methods and describe their characteristics
  Analytical
  Simulation
  Measurements
List the basic steps for a performance study
Apply the steps to formulate a performance study for a given system and goals
Define the difference between validation and verification