## Slide 1: Probability Review
CSCE 654
Computer Communication Networks
Dr. Scott Graham
Department of Electrical and Computer Engineering
Air Force Institute of Technology
(Material from Dr. Barry Mullins & Dr. Scott Midkiff is gratefully acknowledged)

## Slide 2: Outline
Probability theory
Random variables
Stochastic processes
Example processes
  Poisson process
  Exponential process

## Slide 3: Reading
“Appendix: Probability Theory Review” in T. G. Robertazzi, Computer Networks and Systems, 3rd edition.

## Slide 4: Need for Probability
Many network phenomena are not deterministic in nature, such as …
  Packet arrival times
  Packet lengths (service times)
  Number of users
  Channel conditions (error rates)
  Link and node failures
So, we cannot study network performance without utilizing …
  Probability theory
  Random variables
  Random processes

## Slide 5: Probability Theory
“The comparatively late rise of the theory of probability shows how hard it is to grasp, and the many paradoxes show how clearly that we, as humans, lack a well grounded intuition in this matter.” The Art of Probability, Richard Hamming

## Slide 6: Intuitive Definition of Probability
Relative frequency
  If an event A occurs nA times out of n tries, then

## Slide 7: Basic Definitions (1)
A random experiment is an experiment for which the result is not known a priori
  How many “heads” will occur if I flip a fair coin 10 times?
A possible outcome is a sample point
The sample space S is the set of all sample points, i.e., the set of all possible outcomes
  There are 210 = 1024 different outcomes of flipping a coin 10 times
  A simplified sample space with 11 outcomes (0 to 10 occurrences of heads) is valid for our experiment
Notes: EXAMPLES:
Random experiment ---> tossing a fair die
Sample space -----> {1, 2, 3, 4, 5, 6}
Event ------> A = {2, 4, 6} (outcome is even)

## Slide 8: Basic Definitions (2)
An event A is a subset of S
  For example, we could define the event that there are …
    5 “heads”
    An odd number of “heads”
    7 or more “heads”
  The sample space S is also the certain event
    There are 0 to 10, inclusive, “heads”

## Slide 9: Axiomatic Definition of Probability (1)
A probability measure defined on S is a function that associates to each possible event A a real number P(A ) such that:

## Slide 10: Axiomatic Definition of Probability (2)
Example:
  Consider the event that there are 9 or more “heads” when we flip a fair coin 10 times, i.e., that there are 9 “heads” or 10 “heads”
  These two outcomes are mutually exclusive, so P(number of heads  9) = P(number of heads = 9) + P(number of heads = 10)
  P(number of heads = 9) = 10/1024 and P(number of heads = 10) = 1/1024, so P(number of heads  9) = 11/1024

## Slide 11: Probability Laws
The following laws (and many others) can be derived from the definition
Notes: 1. 1 - P(A)
2. 0
3. P(A) + P(B) - P(AB)

## Slide 12: Conditional Probability
The conditional probability of event A given that event B has occurred, denoted by P(A|B), is defined as
Two events are statistically independent iff
If events A, B, C, … are independent, then
Notes: Independent iff P(AB) = P(A) P(B), or P(A|B) = P(A)

## Slide 13: Random Variables
A random variable (r.v.) associates a real number to each event.
The r.v. is continuous if it takes on an uncountably infinite number of distinct values
  For example, the time between packet transmissions
The r.v. is discrete if it takes on a finite or countably infinite number of values
  For example, the number of packet transmissions during a one-hour interval

## Slide 14: Cumulative Distribution Function (CDF)
We define the Cumulative Distribution Function, CDF of r.v. X as
Some properties
Notes: a) 1
b) 0

## Slide 15: Example: CDF for Uniform Distribution
Suppose r.v. X is uniformly distributed in the interval (a, b)
The CDF is given below
a
1
b
x
FX(x)

## Slide 16: Probability Density Function (pdf)
We define the pdf of a continuous r.v. X as
Some properties
Notes: a) 1

## Slide 17: Example: pdf for Uniform Distribution
The r.v. X is uniformly distributed in the interval (a, b), as in the previous example
The pdf is given below
a
1
b
x
FX(x)
1/(b-a)

## Slide 18: Probability Mass Function (pmf)
We define the pmf of a discrete r.v. X as
Some properties
Notes: 1

## Slide 19: Joint Density and Distribution
The joint distribution function of continuous r.v.’s X and Y is
The joint density function of continuous r.v.’s X and Y is

## Slide 20: Marginal Density Function
joint pmf
For a continuous r.v.
For a discrete r.v.

## Slide 21: Independence
A collection of random variables is said to be independent if the joint probability density function is equal to the product of the marginal pdfs
If X and Y are independent random variables, then E[XY] = E[X]E[Y]
  But, note that this is not an if and only if! This means that E[XY] = E[X] E[Y] by itself does not guarantee independence

## Slide 22: Mean or Expectation
The mean (or expected value or expectation or first moment) of a continuous r.v. is
The mean of a discrete r.v. is

## Slide 23: Example: Mean Packet Length
A source produces packets of sizes 40 bytes, 150 bytes and 400 bytes, with probabilities ½, ¼, and ¼, respectively
Define X as the length of a packet produced by the source
  A discrete random variable
We can calculate the mean of X (click)
  E[X] = (1/2) 40 + (1/4) 150 + (1/4) 400 = 157.5 bytes

## Slide 24: Second and n th Moments
For a continuous r.v.
For a discrete r.v.

## Slide 25: Variance and Standard Deviation
The variance
The standard deviation
Notes: - Independent if P(AB) = P(A)P(B)
therefore, P(A|B) = P(A)

## Slide 26: Properties
Some additional properties (where a is a constant)
Notes: A) a E[X]
b) E[X] + E[Y]
c) a^2 Var[X]

## Slide 27: Stochastic Processes
A stochastic process (or random process) is a family of random variables {X(t): t  T} indexed by parameter t over index set T
  The typical interpretation is that T is the time dimension and r.v. X is a function of time
Continuous-time versus discrete-time
  The r.v. takes new values at some point of time in continuous versus discrete time
Continuous-value versus discrete-value
  The r.v. takes on continuous versus discrete values

## Slide 28: First and Second Order Statistics
Mean (continuous case)
Variance (continuous case)
Note that, in general, moments are a function of t
Notes: - Independent if P(AB) = P(A)P(B)
therefore, P(A|B) = P(A)

## Slide 29: Autocorrelation Function
The autocorrelation function is the joint moment of two variables X(t1) and X(t2)

## Slide 30: Poisson and Exponential Distributions
The Poisson and exponential distributions are often used in queuing models
  Basis for the M/M/1 and similar queues
The arrival process is Poisson
  The number of arrivals, e.g., packet transmission attempts, during a given interval of time follows a Poisson distribution
The service process is exponential
  The time to service a “customer,” e.g., transmit a packet, is exponentially distributed

## Slide 31: Poisson Process (1)
A stochastic process {A(t)½t ³ 0} taking nonnegative integer values is said to be Poisson with rate l if
  A(t) is a counting process that represents the total number of events (arrivals) from 0 to time t
    A(0) = 0; and for s < t, A(t) - A(s) equals the number of arrivals in the interval (s,t ]
  The number of arrivals that occur in disjoint time intervals are independent
  The number of arrivals in any interval of length  is Poisson distributed with parameter lt, i.e., for all t, t > 0

## Slide 32: Poisson Process (2)
Dt
t
Arrivals occur with rate l
Probability exactly one customer arriving within the interval
[ t, t + Dt ] = l Dt
Probability no arrivals within the interval [ t, t + Dt ] = 1 - l Dt
As we let Dt approach 0, we have a Poisson process

## Slide 33: Poisson Process (3)
For a Poisson process with parameter , the probability mass function (pmf) is
This is the probability of n occurrences (arrivals) during a period of time of length  if the rate is 

## Slide 34: Expected Value of the Poisson Process
Let the random variable X = A(t+) - A(t) be the number of arrivals during any interval of length 

## Slide 35: Exercise 1
Noise impulses occur on a telephone line according to a Poisson process of rate l. What is the probability that no impulses occur during the transmission of a message that is t seconds long?
Solution:

## Slide 36: Properties of the Poisson Process (1)
1) Interarrival times are independent and exponentially distributed with parameter l (the rate parameter)
  If tn is the time of the nth arrival, the intervals tn = tn+1 - tn have the following cumulative distribution function (CDF) and are mutually independent
t1
tn
t3
t2
tn+1
t1
tn
t2
exponential CDF

## Slide 37: Properties of the Poisson Process (2)
Let t = time between successive arrivals in a Poisson process; t is a random variable
  For the Poisson process, interarrival times are exponentially distributed random variables
  Distribution and density functions for an exponentially distributed random variable …
CDF
= Probability inter-arrival time £ t
= probability that something arrived in time t
= the negation that nothing arrived in time t

## Slide 38: Properties of the Poisson Process (3)
2) If k independent Poisson processes A1, ..., Ak, with rates l1, ..., lk, are merged into a single process, A = A1 + … + Ak, the combined process A is Poisson with rate l = l1 + … + lk
l1
l2
lk
...
l
+
l1
l2
lk
...
l
+

## Slide 39: Properties of the Poisson Process (4)
3) If a Poisson process (with rate l) is split into k other process by independently assigning each arrival to the i th process with probability pi, p1 + ... + pk = 1, the resulting k processes are Poisson with rate pi l for the i th process
p1l
...
l
p2l
pkl

## Slide 40: Appropriateness (1)
Poisson process is generally a good model if there are a large number of users (packet sources) such that
  The users are similar
  The users are independent
Is the Poisson process appropriate?

## Slide 41: Appropriateness (2)
Suppose that we merge n independent and identically distributed arrival processes (not necessarily Poisson)
  Each process has rate l / n, so the aggregate rate is l
  The interarrival times, t, for each process have a distribution F(s) = P {t £ s} and are independent
  The aggregate process approximates a Poisson process with rate l as n ® ¥ under mild conditions

## Slide 42: Example 1 using the Poisson Process
Suppose a computer installation has a library of 100 subroutines and that each week on the average, bugs are found (and corrected) in two of the subroutines. Assume the number of subroutines per week with newly discovered bugs follows a Poisson process. Calculate the probability that errors will be found in not more than three subroutines next week.

## Slide 43: Example 2 using the Poisson Process
Suppose it has been determined that the number of inquiries that arrive per second at the central computer can be described by a Poisson random variable with an average rate of 10 messages per second. 1) What is the probability that no inquiries arrive in a one- second period? 2) What is the probability that 15 or fewer inquiries arrive in a one second period?

## Slide 44: Exponential Distribution (1)
A random variable has an exponential distribution with parameter m if sn is the nth value,
Parameter m is interpreted as the service rate (customers served per unit time when the server is busy)
For queues, we assume that service times sn are mutually independent and, also, independent of the interarrival times
  Implies that the length of an arriving packet does not affect the arrival time of the next packet

## Slide 45: Exponential Distribution (2)
The CDF of the nth instance of the r.v. is
The expected value is of the nth instance of the r.v. is

## Slide 46: Exponential Distribution: Density Function
Cumulative distribution function (CDF):
Density function (pdf), f(sn):

## Slide 47: Exponential Distribution: Mean
Expected value (mean) of sn, E[sn]:

## Slide 48: Exponential Distribution: Other Statistics
Second moment of sn, E[sn2]:
  the expected value of the square of the deviations of a random variable from the point of origin
Variance of sn, V(sn):
Standard deviation of sn, S(sn):

## Slide 49: Example with Exponential Distribution
If the time an engineer spends in a session at a terminal has an exponential distribution with an average value of 36 minutes, find
  The probability that an engineer will spend 30 minutes or less at the terminal
  The probability the engineer will use it for more than one hour
  If an engineer has already been at the terminal for 30 minutes, what is the probability that he will spend more than another hour at the terminal?

## Slide 50: Exponential Distribution is Memoryless (1)
The exponential distribution is memoryless, i.e., the process after time t is independent of what occurred prior to time t
For service times:
  The additional time needed to complete a customer’s service in progress is independent of when the service started

## Slide 51: Memoryless Property (2)
The memoryless property allows the use of Markov chains to analyze the M/M/1 queue
  Given the independence of inter-arrival times and service times, the future number of customers in the system depends only on N(t), the number of customers in the system at time t
The exponential r.v. is the only continuous r.v. that has the memoryless property
  See proof in Robertazzi
The geometric distribution is the discrete distribution with the memoryless property

## Slide 52: Example of Memoryless Property
Trains arrive at a station according to a Poisson process with mean arrival rate of 1 train each 20 minutes. You get to the station and are told the last train arrived 19 minutes ago. What is the expected time until the next train arrives?
Solution:
Inter-arrival time is exponentially distributed with mean 20 minutes. Due to the memoryless property, the expected time until the next train arrives is 20 minutes.

## Slide 53: You should now be able to … (1)
Define random experiment, sample space, and event
Define and apply
  Basic properties of probability
  Probability distribution functions
  Probability density functions
  Probability mass functions
  Joint probabilities
  Conditional probabilities
Calculate the expectation (mean), nth moment, variance, and standard deviation

## Slide 54: You should now be able to … (2)
Determine if a set of random variables are independent
Define a stochastic process
Define and utilize properties of Poisson processes and exponential processes