## Slide 1: Queuing Theory: M/M/1 Queue
CSCE 654
Computer Communication Networks
Dr. Scott Graham
Department of Electrical and Computer Engineering
Air Force Institute of Technology
(Material from Dr. Barry Mullins & Dr. Scott Midkiff is gratefully acknowledged)

## Slide 2: Outline
Motivation
Introduction to queuing systems
  Elements of a queuing system
  Queuing system notation
Background
  Arrival and departure processes
Little’s Law
M/M/1 queue
  Derivation and results
  Application to analysis of multiplexing
Burke’s Theorem

## Slide 3: Reading
T. G. Robertazzi, Computer Networks and Systems, 3rd edition.
  Chapter 1: Introduction to queuing models
  Sections 2.1-2.2: The M/M/1 queuing system
  Section 2.3: Little’s Law

## Slide 4: Queuing or Queueing?
From Merriam-Webster’s Collegiate Dictionary:
Main Entry: 2queue Function: verb Inflected Form(s): queued; queu·ing or queue·ing Date: 1777
transitive senses: to arrange or form in a queue
intransitive senses: to line up or wait in a queue – often used with up

## Slide 5: Motivation (1)
Analytic models based on queuing theory can often be used to predict the effects of some change in load or design
  Assumptions are usually necessary for analysis
Basic concept
  “Customers” arrive for service and, if all servers are busy, the customer is queued and serviced later
  Parameters: arrival rate, service rate, number of servers
  Measures: wait time, service time, time in system, server utilization, number in queue, number in system, …

## Slide 6: Motivation (2)
Single queue systems are often used to represent shared resource networks
Networks of queues can often be used to represent other types of networks
  Process networks
  Switching networks
Shared Resources
User 1
User N
…

## Slide 7: Examples (1)
Time-shared computer
  Customers: Programs (processes)
  Severs: CPU, disk, I/O devices, bus, …
Packet-based statistical multiplexer
  Customers: Packets (or cells)
  Server: Link
Circuit-switched or channel-based concentrator
  Customers: Calls
  Servers: Channels

## Slide 8: Examples (2)
Multiple access network, such as an Ethernet LAN or wireless LAN
  Customers: Packets (frames)
  Server: Medium, e.g., fiber, twisted pair, RF medium
Web (or other) services
  Customers: Client requests
  Server: Web (or other) server

## Slide 9: What Can We Study?
Factors
Number of users
Use pattern (workload)
Service characteristics
Amount of resource
Performance
Waiting time
Blocking
Losses

## Slide 10: Elements of a Queue
Input
Output
Queue
Server

## Slide 11: Basic Model (1)
“Customers” from some population arrive at the system at random arrival times
 is the customer arrival rate
Queuing system has m identical servers
The jth customer seeks a service that will require sj units of service time from one server
If all servers are busy, arriving customer joins a queue until a server is available

## Slide 12: Basic Model (2)
Service discipline specifies the order in which customers are selected from the queue
  Examples: FIFO, LIFO, priority, fair queuing, …
Waiting time wj is the time that the jth customer is made to wait between entering the system and entering service
Total delay in the system rj = wj + sj
n  number of customers in the system
  A random variable
nq  number of customers in the queue
  A random variable

## Slide 13: Rules for All Queues
Key variables used in queuing analysis will be introduced and the relationships between them discussed
1
2
m
Arrival
Waiting
Service


n
nq
ns

w
s
r
Previous
Arrival
Arrival
Begin
service
End
service

## Slide 14: Rules for All Queues
Key variables
   = interarrival time, the time between two successive arrivals
   = Mean arrival rate = 1/E[]. This can sometimes be a function of the state of the system.
  s or t = service time per customer
   = mean service rate = 1/E[s]. Total service rate for m servers is m
  n = number of customers in system. (Including those receiving service)
  nq = number of customers waiting to receive service
  ns = number of customers receiving service
  r = response time or total time in the system (waiting and service)
  w = waiting time or the time spent in the queue
All the above except  and  are random variables

## Slide 15: Delay Components (1)
1) Processing delay: time from when packet is correctly received until it is assigned an outgoing link
2) Queuing delay: time from when packet is assigned an outgoing queue until transmission begins (wait time)
processing
queuing
transmission
propagation

## Slide 16: Delay Components (2)
3) Transmission delay: time from when first bit of packet is transmitted until last bit is transmitted
4) Propagation delay: time from when last bit is transmitted by sender until last bit is received
processing
queuing
transmission
propagation

## Slide 17: Delay Components (3)
If we assume adequate computational resources, processing delay is independent of amount of traffic
Propagation delay is a property of the transmission medium and is independent of the amount of traffic
Queuing delay and transmission delay depend on the amount of traffic and the length of packets
Traditional focus of performance models and queuing theory is on …
  Queuing delays
  Transmission delay

## Slide 18: Queuing Notation (1)
Suppose you are waiting in a queue with other students waiting to use some PCs. The service facility has a certain number of computers available, but if all the computers are busy, the arriving students must wait.
In queuing theory terms, the students are customers.
There are 6 elements used to specify a queue
1. Arrival
process
2. Service time
distribution
3. Number of servers
4. Waiting positions
6. Service discipline
5. Customer population

## Slide 19: Queuing Notation (2)
Arrival Process
  If customers arrive at times t1, t2, …,tj, the random variables j = tj – tj-1 are called the interarrival times. The general assumption about j’s is that they are IID (independent and identically distributed)
  The most common arrival process is Poisson which means that the interarrival times are independent and exponentially distributed
Service Time Distribution
  This distribution specifies how much time each customer spends receiving service. The most common distribution used for this is exponential.
Number of Servers
  This element is used to specify how many identical servers are contained in the system. If the servers are not identical, they are usually separated into another queuing system

## Slide 20: Queuing Notation (3)
System Capacity
  This specifies the number of customers that may be waiting for and receiving service at any one time
Population Size
  The total number of potential customers
    Often modeled as infinite but doesn’t have to be
Service Discipline
  The order in which customers are served
  Typically FCFS, other options: (LCFS, LCFS-PR, RR, PS, etc.)
Queuing systems use a shorthand notation to specify the above six elements – called Kendall notation

## Slide 21: Kendall Notation
This notation has the form A/S/m/B/K/SD A – arrival process S – service distribution
m – number of servers
B – system capacity (Max # that can be in system (waiting and in service) K – customer population
SD – service discipline
The distributions used in A and S have some commonly used abbreviations
M – memoryless (Markovian) (exponential)
Ek – Erlang with parameter k
Hk – Hyperexponential with parameter k
D – deterministic (constant)
G – general (any)

## Slide 22: Time Averages (1)
At time t > 0, let:
  N(t) = Number of customers in the system at time t
  (t) = Number of customers that arrived in the interval [0, t]
  ri = Time spent in the system by the ith customer to arrive
These each form a stochastic process
Suppose we observe these values for a system over time

## Slide 23: Time Averages (2)
time
N(t)
arrivals:
departures:
The time average of n() up to time t:

## Slide 24: Time Averages (3)
In general, N(t) will change with time, but many systems are such that N(t) will tend to the steady-state time average N as t increases, or
Arrival rate:
Customer delay:
  N(t) = Number of customers in the system at time t
  () = Number of customers that arrived in the interval [0,t]
  ri = Time spent in the system by the ith customer to arrive

## Slide 25: Little’s Theorem
N, , and T are related by a simple formula (the result is known as Little’s Theorem)
  The expected number in the system (queue) is equal to the arrival rate times the expected time in the system (queue).
N = T
Assumptions for derivation
  The system is initially empty, N(0) = 0
  Customers depart the system in the order that they arrive
    i.e., first-come first-served

## Slide 26: Little’s Law
Consider
  The arrival rate (l)
  The number in the system, N(t), number in queue, nQ(t), or the number in service, nS(t)
  The time in the system, r, time in queue, w, or in service, s
These are related by Little’s Law
  Number in system: E[n] = l E[r]
  Number in queue: E[nQ] = l E[w]
  Number in service: r = E[nS] = l E[s]

## Slide 27: Utilization
The utilization of a single server system is
The utilization of a c-server system is

## Slide 28: Exercise 1
Over the course of a day, customers enter a store at an average rate of 32 customers per hour. The average customer spends 12 minutes inside. How many customers do we expect to find in the store at any given time?
Solution:
l = 32/hour
T = 12 min = 0.2 hour
N = l T = 32(0.2) = 6.4 customers

## Slide 29: Transmission Line (1)
m
Source
Destination
l
packet arrival rate
NQ packets in queue
1/m = X = transmission time

## Slide 30: Transmission Line (2)
Parameters
  l is the arrival rate
  NQ is the average number of packets waiting in queue (not being transmitted)
  W is the average waiting time spent in queue (not including transmission time)
Little’s Law gives NQ = lW
If X is the average transmission time, Little’s Theorem gives the utilization r (the average number of packets under transmission) as

## Slide 31: Transmission Line (3)
Consider the case where …
1/l is the expected interarrival time
If r > 1, then the expected service time is greater than the expected interarrival time, i.e., customers arrive faster than they can be serviced!
  Queue will overflow, or grow infinitely long
  r  1 results in an unstable situation

## Slide 32: Network of Transmission Lines (1)
Network
lm
l1
l2
l3
l4
l5
l6
l7
...

## Slide 33: Network of Transmission Lines (2)
Packets arrive at m different nodes for transmission with rates l1, l2, ..., lm
N is the total number of packets in the network
Little’s Law gives the average delay per packet

## Slide 34: Network of Transmission Lines (3)
Note that the average delay per packet is independent of packet length distribution and the method for routing packets!
Also, for node i, Ni = liTi

## Slide 35: Window-Based Flow Control (1)
Consider a window flow control with window size WS
  The number in the system, N, must be s.t.
  N = lT £ WS
Little’s Law gives lT £ WS, where T is the average time in the system (in queue and in service)
If congestion occurs, T increases, so l must decrease
  If the time packets spend in the system is increasing, we need fewer packets to arrive so that the window is not exceeded

## Slide 36: Window-Based Flow Control (2)
Suppose that the system is congested and can deliver packets at a rate l for each session
  If acknowledgment delays are negligible w.r.t. forward packet delays, then WS  lT
  Increasing WS for all sessions will only serve to increase delay T

## Slide 37: Arrival Statistics: the Poisson Process
A stochastic process {A(t) | t ≥ 0} taking nonnegative integer values is said to be Poisson with rate  (arrival rate) if
  A(t) is a counting process that represents the total number of arrivals from 0 to time t,
    i.e., A(0) = 0; and for s < t, A(t) - A(s) equals the number of arrivals in the interval (s,t]
  The number of arrivals that occur in disjoint time intervals are independent
  The number of arrivals in any interval of length  is Poisson distributed with parameter ,
    i.e., for all t,  > 0
    Pn(t) = P[number of arrivals by time t = n ]

## Slide 38: Expected Value of the Poisson Process
Let the random variable X = A(t+) - A(t) be the number of arrivals during any interval of length 

## Slide 39: Properties of the Poisson Process (1)
1) Interarrival times are independent and exponentially distributed with parameter  (the rate parameter) If tn is the time of the nth arrival, the intervals n = tn+1 - tn have the probability distribution and are mutually independent
t1
tn
t3
t2
tn+1
1
n
2

## Slide 40: Background: The Poisson Process
Dt
t
Arrivals occur with rate l
Probability [exactly one customer arriving within the interval
  [ t, t + Dt ] ] = l Dt
Probability [no arrivals within the interval [ t, t + Dt ] ] = 1 - l Dt
As we let Dt approach 0, we have a Poisson process

## Slide 41: Arrival Distribution
The Poisson Distribution
Let Pn(t) = P[number of arrivals by time t = n]

## Slide 42: Number of Arrivals
Let n be the mean number of arrivals in an interval of length t
  Mean
  Variance

## Slide 43: Appropriateness (1)
Poisson process is generally a good model if there are a large number of users (packet sources) such that
  The users are similar
  The users are independent
Is the Poisson process appropriate?

## Slide 44: Appropriateness (2)
Suppose that we merge n independent and identically distributed arrival processes (not necessarily Poisson)
  Each process has rate l / n, so the aggregate rate is l
  The interarrival times, t, for each process have a distribution F (s) = P {t ≤ s} and are independent
  The aggregate process approximates a Poisson process with rate l as n ® ¥ under mild conditions

## Slide 45: Example 1 using the Poisson Process
Suppose a computer installation has a library of 100 subroutines and that each week on the average, bugs are found (and corrected) in two of the subroutines. Assume the number of subroutines per week with newly discovered bugs follows a Poisson process. Calculate the probability that errors will be found in not more than three subroutines next week.

## Slide 46: Example 2 using the Poisson Process
Suppose it has been determined that the number of inquiries that arrive per second at the central computer can be described by a Poisson random variable with an average rate of 10 messages per second. 1) What is the probability that no inquiries arrive in a one- second period? 2) What is the probability that 15 or fewer inquiries arrive in a one second period?

## Slide 47: Interarrival Times
Let T = time between successive arrivals in a Poisson process
  T is a random variable
  For the Poisson process, interarrival times are exponentially distributed random variables
  Distribution and density functions for an exponentially distributed random variable …

## Slide 48: Service Statistics: the Exponential Distribution
Service times have an exponential distribution with parameter  If sn is the the service time of the nth customer,
Parameter  is the service rate (customers served per unit time when the server is busy)
Service times sn are mutually independent and independent of the interarrival times
  Implies that the length of an arriving packet does not affect the arrival time of the next packet

## Slide 49: Exponential Distribution: Density Function
Cumulative distribution function, or simply the distribution function:
Density function, p(sn):

## Slide 50: Exponential Distribution: Mean
Expected value (mean) of sn, E[sn]:
&

## Slide 51: Exponential Distribution: Other Statistics
Second moment of sn, E[sn2]:
  the expected value of the square of the deviations of a random variable from the point of origin
Variance of sn, V(sn):
Standard deviation of sn, S(sn):
&

## Slide 52: Exponential Distribution is Memoryless (1)
The exponential distribution is memoryless, i.e., the process after time t is independent of what occurred prior to time t
For service times:
  The additional time needed to complete a customer’s service in progress is independent of when the service started

## Slide 53: Exponential Distribution is Memoryless (2)
For interarrival times:
  The time for the next arrival is independent of when the last arrival occurred
The memoryless property allows the use of Markov chains to analyze the M/M/1 queue
  Given the independence of interarrival times and service times, the future number of customers in the system depends only on N(t), the number of customers in the system at time t

## Slide 54: Example with Exponential Distribution
If the time an engineer spends in a session at a terminal has an exponential distribution with an average value of 36 minutes, find
  The probability that an engineer will spend 30 minutes or less at the terminal
  The probability the engineer will use it for more than one hour
  If an engineer has already been at the terminal for 30 minutes, what is the probability that he will spend more than another hour at the terminal?

## Slide 55: Markov Property (1)
As we will see, the memoryless property of service time and interarrival times allows the use of Markov chains to analyze the M/M/1 queue
Given the independence of interarrival times and service times, the future number of customers in the system depends only on N(t), the number of customers in the system at time t

## Slide 56: Markov Chain Formulation (2)
The future number of customers in the system depends only on N(t), the number in the system at time current time t
  {N(t) t  0} is a continuous-time Markov chain
We can analyze the process as a discrete-time Markov chain by dividing time into small increments of duration 
  Consider times 0, , 2, 3, ..., k, ...
  Nk = Number of customers at time k = n(k)
  {Nk k = 0, 1, ...} is a discrete-time Markov chain
  Nk is the state of the process

## Slide 57: Markov Chain Formulation (3)
If the process is in state i (Nk = i), there is a fixed probability that it will next be in state j (Nk+1 = j), Pij regardless of its history prior to reaching state i
The Pij’s are the transition probabilities
Must satisfy:

## Slide 58: Markov Property (4)
b
c
a
If we know that the system is in state a at time tk, the probability of transition to any another state at time tk+1 can be determined
  No additional history is needed
pa,a
pa,c
pa,b
pa,a + pa,b + pa,c = 1

## Slide 59: Markov Chain Formulation (5)
The process is a birth-death process -- new customers may enter the system (a birth) or leave the system (a death)
If  is small enough, then at most one customer may enter or leave the system during one interval

## Slide 60: Markov Chain Formulation (6)
Let a = P{arrival} and d = P{departure}
0
1
2
n-1
n
n+1
...
1-a
d(1-a)
a
(1-a)(1-d)+ad
a(1-d)
a(1-d)
a(1-d)
d(1-a)
d(1-a)
d(1-a)
(1-a)(1-d)+ad

## Slide 61: Markov Chain Formulation (7)
Consider Pii (stay in the same sate):

## Slide 62: M/M/1 Queues
Single queue
Single server (single transmission line)
Customers (packets) arrive according to a Poisson process with rate l per second (s-1)
The service time distribution is exponential with mean 1/m seconds
Infinite buffer
m
l

## Slide 63: Markov Chain
0
l
m
1
2
j
j+1
l
l
m
m
Due to the memoryless property of exponential random variables, the number of customers in the system at time t, N(t), can be expressed as a continuous-time Markov chain

## Slide 64: Probability Flux
The probability flux along a transition is the product of the probability of the state at which the transition originates and the transition rate associated with the transition
  Indicates the mean number of times per second that the event corresponding to the transition occurs
In steady-state, the mean number of times/sec a state is entered equals the mean number of times/sec the state is departed
  Leads to the global balance equations

## Slide 65: Global Balance
Total rate of transitions out of state n equals total rate of transitions into state n
  Dynamic equilibrium
l
m
l
m
l
m
l
m
n+1
n-1
n

## Slide 66: Global Balance Equations
Global balance equations for the M/M/1 queue:
If there were N states, there would be N equations, plus the following relation to normalize the values
l
m
n-1
l
m
n
n+1
l
m
l
m

## Slide 67: Local Balance
l
m
l
m
l
m
l
m
n+1
n-1
n
For some Markov chains, the rate of transitions from state A to state B is equal to the rate of transition from B to A
  For example, the rate of transitions from n-1 to n equals the rate of transitions from n to n-1

## Slide 68: Local Balance Equations
Local balance equations for the M/M/1 queue:

## Slide 69: Solving Local Balance Equations (1)
The local balance equations yield the following n-1 recursions:

## Slide 70: Solving Local Balance Equations (2)
Normalization is achieved through the “conservation of probability”

## Slide 71: Solving Local Balance Equations (3)
Let r = l/m and use the following identity
Then …

## Slide 72: Results (1)
When  = / < 1, we get …
The utilization is …
The expected value of n (number of customers in system) is …

## Slide 73: Results (2) Expected Number of Customers in the System
Let
&

## Slide 74: Results (3)
Using Little’s Law, we can find the expected time in the system …
And, the expected time in the queue (average waiting time) …
N

## Slide 75: Results (4)
Applying Little’s Law again, we can find the expected number in the queue …
We can also derive the average number of customers in service
This verifies our previous interpretation of  as the utilization of the server (link or channel) – the long-term proportion of time the server is busy

## Slide 76: M/M/1 Queue Graphical Results
Expected number of customers in system, N
Note that as   1, N  

## Slide 77: Exercise
A concentrator receives messages from a group of terminals and transmits them over a single transmission line. Suppose that messages arrive according to a Poisson process at a rate of one message every 4 ms, and that message transmission times are exponentially distributed with mean 3 ms.
  (a) Find the mean number of messages in the system and the mean total delay.
  (b) What percentage increase in arrival rate results in doubling the above mean total delay?

## Slide 78: Exercise Solution (1)
(a) Find the mean number of messages in the system and the mean total delay.
  Mean number of messages
  Mean delay

## Slide 79: Exercise Solution (2)
(b) What percentage increase in arrival rate results in doubling the above mean total delay?
A 16.7% increase

## Slide 80: M/M/1 Example
On a network gateway, measurements show that the packets arrive at a mean rate of 125 packets per second (pps) and the gateway takes about 2 milliseconds to forward them. Using an M/M/1 model, analyze the gateway. What is the probability of buffer overflow if the gateway had a total capacity of 12?
arrival rate l = 125 pps
service rate m = 1/0.002 = 500 pps
utilization r = l/m = 125/500 = 0.25
probability of n packets in gateway = (1-r)rn = 0.75(0.25)n
mean number of packets in gateway = r/(1-r) = 0.25/0.75 = 0.33
mean time spent in gateway = (1/m)/(1-r) = (1/500)/(1-0.25) = 2.66ms

## Slide 81: M/M/1 Example
On a network gateway, measurements show that the packets arrive at a mean rate of 125 packets per second (pps) and the gateway takes about 2 milliseconds to forward them. Using an M/M/1 model, analyze the gateway. What is the probability of buffer overflow if the gateway had a total capacity of 12?
probability of buffer overflow =
P(13 or more packets in gateway) = r13 = 0.2513 = 1.49x10-8

## Slide 82: Traffic Multiplexing
Consider a communication link
  Fixed transmission capacity (C), the rate at which bits can be transmitted (bits per second)
  Several traffic streams may share the capacity
  The scheme for sharing can affect performance
Forms of multiplexing
  Statistical multiplexing
  Separate channels
    Time-division multiplexing (TDM)
    Frequency-division multiplexing (FDM)

## Slide 83: Statistical Multiplexing
Packets from all traffic streams are merged into a single queue and transmitted on a first-come first-served (FCFS) basis
  TSM=L/C seconds needed to transmit L-bit packet
  May also maintain a separate queue for each traffic stream and service in a “round-robin” manner (skipping over an empty queue with no loss of transmission capacity)
Service Rate m = C/L

## Slide 84: Time-Division Multiplexing (1)
Time on the channel is divided into m slots and each of m traffic streams is given one slot
  Create m channels, each with capacity C/m
  L-bit packet takes TTDM = Lm/C seconds to transmit if packets are long compared to the length of a slot
  L-bit packet takes TTDM = L/C seconds to transmit if slots are of packet length, but must wait (m-1) slots between transmissions

## Slide 85: Time-Division Multiplexing -- TDM (2)
Service time: 1/mi = Lm/C (i = 1,2,…,m)
Service rate: mi = C/Lm
t
...
1
2
m
...
1
2
m
1
m1
m2
mm
...

## Slide 86: Frequency-Division Multiplexing -- FDM
Frequency-division multiplexing (FDM): channel bandwidth W is subdivided into m channels and each of m traffic streams is given one channel
  Create m channels, each with bandwidth W/m, or capacity C/m (ignoring guard bands between channels)
  L-bit packet takes TFDM=Lm/C seconds to transmit

## Slide 87: Multiplexing Performance (1)
We will see that statistical multiplexing has smaller average delay than either TDM or FDM
  Channel capacity is wasted with TDM (wasted time slot) and FDM (wasted bandwidth) when a traffic stream is idle
  Transmission time greater for TDM and FDM
Advantages of TDM or FDM
  Statistical multiplexing has lower average delay, but higher variance of delay
  TDM and FDM eliminate the need to identify traffic stream associated with each packet

## Slide 88: Multiplexing Performance (2)
We can use the results for the M/M/1 queue to analyze statistical multiplexing (SM) versus time division multiplexing (TDM) or frequency division multiplexing (FDM)
Assume:
  m statistically identical and independent Poisson packet streams, each with arrival rate l/m, are transmitted over a single communication channel
  Packet lengths for all streams are independent and exponentially distributed with average transmission time 1/m

## Slide 89: Multiplexing Performance (3)
Statistical multiplexing combines m streams of packets and transmits them over a single stream
TDM and FDM keep the m streams separate using separate channels
/m
/m
/m
...


statistical multiplexing
/m
/m
...
/m
/m
TDM or FDM

## Slide 90: Multiplexing Performance (4)
For statistical multiplexing:
For TDM (or FDM):
An average packet spends m times longer in queue and in service with TDM or FDM than it does with statistical multiplexing
  However, we have not considered variance

## Slide 91: Burke’s Theorem
A stochastic process is reversible if the samples
{X(t1), X(t1), …, X(tm)}
have the same distribution as
{X(-t1), X(- t2), …, X(- tm)}
for every  and every t1, t2, …, tm
Burke’s Theorem: The departure process from an M/M/1 queuing system, in equilibrium, is Poisson
  Proof, based on reversibility, is given in Robertazzi, Section 2.4)
More later with networks of queues …

## Slide 92: You should now be able to …
Define a Poisson process, identify its main properties, and characterize interarrival times
Use the a/b/m/K shorthand notation to describe queuing systems
Apply Little’s formula to analyze queues
Model M/M/1 queues as Markov chains
Derive and apply results for M/M/1 queues