## Slide 1: Network Design: Theoretical Approach
CSCE 654
Computer Communication Networks
Dr. Scott R. Graham
Department of Electrical and Computer Engineering
Air Force Institute of Technology
(Material from LTC Bob McTasney, Maj Tom Dube, Maj Ryan Thomas, Maj Scott R. Graham, Dr. Barry Mullins & Dr. Scott Midkiff is gratefully acknowledged)

## Slide 2: Outline
Network design problem
Topology design problem
  Capacity
  Delay
  Reliability
  Cost
General capacity assignment problem
  A brief review of queuing theory

## Slide 3: Packet-Switched Network Design (1)
B
D
C
A
E
F
I
J
H
G
0
3
30
8
0
5
20
25
0
…
…
A
B
C
A
B
C
Source
Dest
Given
  Node locations
  Peak-hour traffic rate between nodes

## Slide 4: Packet-Switched Network Design (2)
B
D
C
A
E
F
I
J
H
G
Design variables …
  Network topology
  Channel capacity
  Routing policy
Performance metrics …
  End-to-end delay
  Throughput
  Reliability
  Cost

## Slide 5: Classical Formulation
Minimize total line cost
Subject to constraints …
  Link capacity must exceed some minimum
  Average packet delay cannot exceed maximum
  A certain level of reliability must be provided
Variations
  Minimize average packet delay given maximum network cost
  Maximize throughput given maximum delay and cost
The topology design problem is the optimization problem to be solved

## Slide 6: Topology Design Problem
Topology design problem is very complex
  It is not feasible to determine an optimal solution for real-world problems
  Decomposition and heuristics are needed
Problem decomposed into sub-problems
  Topology design to determine network topology
  Capacity assignment to determine the topology and the capacity of each link
  Flow assignment to determine the routing of traffic over the topology

## Slide 7: “Tools” for Network Design
Requirements analysis (still to come)
Graph theory (still to come)
Optimization (still to come)
Performance evaluation (already covered)
  Queuing models
  Simulation
Network management (still to come)

## Slide 8: Management, Performance, and Design
Performance
Evaluation/Analysis
Network
Design
Network
Management

## Slide 9: Simplified Design Process
determine routing
generate topology
determine cost
check reliability
check delay
check capacity

## Slide 10: Capacity Constraint
check capacity
Given a topology and routing, the capacity can be checked for feasibility
For Link ( i, j ),
  Assigned capacity is Cij
  Traffic arrival rate is Fij
Require that Cij > Fij
If violated, delay on the link will go to infinity
  This condition will violate delay constraint
  So, capacity constraint can be ignored

## Slide 11: Delay Analysis (1)
Given a topology and routing, the delay can be estimated
Let sd be the average packet rate from source s to destination d, then the total network traffic, , is …
check delay

## Slide 12: Delay Analysis (2)
Using the Kleinrock Independence Approximation, the delay over each link, Tij, is …
Average delay in the network, T, is …

## Slide 13: Delay Analysis (3)
Average delay for each source-destination pair, Zsd, can also be determined by summing link delays on the path …

## Slide 14: Network Reliability (1)
check reliability
Reliability is a measure of the topology’s ability to withstand node and link failures
Given a topology, the reliability, can be evaluated
  Topology can be required to be “k-connected”
  Topology can be required to be connected with some probability

## Slide 15: Network Reliability (2)
Nodes i, j  N in graph G = {N, A} are k-connected if all subgraphs G’ that can be formed by deleting at most k-1 nodes, but not nodes i or j, contain a path from node i to node j
2
4
3
5
1
Nodes 1 and 2, 3, 4 are 2-connected
Nodes 1 and 5 are not 2-connected

## Slide 16: Network Reliability (3)
1
3
5
2
4
6
1-connected
2-connected
1
3
5
2
4
6
3-connected
1
3
5
2
4
6
Graph G = {N, A} is k-connected if all subgraphs G’ that can be formed by deleting at most k-1 nodes are connected
  Every pair of nodes is k-connected
  Network will not fail unless k nodes or links fail

## Slide 17: Network Cost (1)
Given a topology, the network cost can be evaluated
The cost of each link depends on a number of factors
  Tariffs
  Service provider
  Capacity (Cij)
  Length
  Technology
  Location
  Environment
determine
cost

## Slide 18: Network Cost (2)
Given that we will have a link from i to j, capacity is the primary design variable
  Cost is a function of capacity Cij
For cost function fij, network cost, D, is
fij
Cij
Simple
fij
Cij
Non-Linear
fij
Cij
Discrete

## Slide 19: Network Cost (3)
The form of cost function fij affects the solution technique
Function fij is usually complex
  Non-linear
  Contains steps, discontinuities
This just considers the fixed costs
  Topological design may affect other cost factors
  Life-cycle costs should be considered
    Operation
    Maintenance
    Capital investment …

## Slide 20: General Capacity Assignment Problem
Given:
Topology and flows, i
Minimize:
Some function of delay, f (E[net])
With respect to:
Link capacities, Ci
Under constraint:
Cost function, D

## Slide 21: Model
Simple delay function
Packet network, with …
  Li  mean packet length at queue i (in bits)
  Ci  link capacity out of queue i (in bps)
Cost constraint, with link costs proportional to capacity

## Slide 22: Mean Offered Load (1)
Expected delay on link i …
Mean traffic (offered load) through queue i in bits per second


## Slide 23: Mean Offered Load (2)
Expressing mean delay in terms of mean offered load
  Link …
  Network …

## Slide 24: Minimization Problem
Minimize …
With respect to …
Under constraint …

## Slide 25: Solution to Minimization Problem (1)
Constraint
(0 if satisfied)
Lagrange
multiplier
Let’s use Lagrange multipliers
Incorporate the constraint and minimize the following with respect to { Ci } and  for M links …

## Slide 26: Solution to Minimization Problem (2)
M equations
1 equation (constraint)
M+1 (non-linear) equations in M+1 unknowns
  Can be solved

## Slide 27: Solution to Minimization Problem (3)

## Slide 28: Interpreting this Result
ri is the absolute minimum Ci
  Since i = ri / Ci < 1
(C –  ri ) is the “excess” network-wide capacity to be distributed among links
This result tells us to distribute the excess capacity in proportion to square root of traffic
 | r_i | C | C_i | % Excess
 | 5 | 50 | 8.69 | 18.5%
 | 5 |  | 8.69 | 18.5%
 | 10 |  | 15.22 | 26.1%
 | 5 |  | 8.69 | 18.5%
 | 5 |  | 8.69 | 18.5%
Totals | 30 | 50 | 50 | 100.0%

## Slide 29: Average Delay
If  is the total arrival rate to the network, then the average delay for the network is …
  Where the network-wide traffic intensity, , is …

## Slide 30: Design Procedure
Simple procedure …
1. From input flows and routing information, find ri using traffic equations
2. Assign Ci according to square root rule

## Slide 31: Example 1: Star Network
Several statistical multiplexers homing on a central host
q1
q3
q2
C1
C2
C3
HOST

## Slide 32: Example 1: Numerical Values
Three offices connected to central database
  Main office: 20 terminals
  Branch office: 5 terminals
  Satellite office: 1 terminal
All user terminals have identical statistics
Mean packet length of 128 bytes
Mean arrival rate of 2,000 packets per second from each terminal
Total available capacity: 64 Mbps

## Slide 33: Example 1: Results (Exercise 1)
Exercise 1: Complete the results for the Branch office.
Office
Main
Branch
Satellite
40
2
40.96
2.048
6400
1431
47.2
3.443
0.164
0.734
KPkts/ second
Mbps
bps1/2
Mbps
ms
10
10.24
3200
13.44
0.328

## Slide 34: Example 1: Average Delay
Average delay of a packet through the network is 0.218 ms
  Sum of delays per source weighted by fraction of traffic

## Slide 35: Example 1: Notes on the Results
The largest arrival rates (Main office) get smallest delays — Is this fair?
  Main: 0.164 ms (40 KPkts/s)
  Branch: 0.328 ms (10 KPkts/s)
  Satellite: 0.734 ms (2 KPkts/s)
Need to extend results to apply to a general topology — here just a simple star topology
Do we really want to minimize mean delay? Or, are there other options?

## Slide 36: General Capacity Assignment Problem
Want to extend to general topologies
  Previous example considered a star topology
Traffic on each link, { i }, determined by …
  Source-destination traffic
  Network topology
  Routing in the network

## Slide 37: Example 2: General Mesh Topology
A
Denver
LA
2
1
Dallas
Chicago
DC
E
D
C
B
5
4
3
7
6
C = 48 Kbps
Average packet length = 1000 bits

## Slide 38: Example 2: Traffic Matrix
0.75
—
0.61
2.4
2.94
0.75
—
0.13
0.63
0.61
0.61
—
0.13
0.82
0.94
2.4
—
0.63
0.82
9.34
2.94
—
0.61
0.94
9.34
A
B
C
D
E
Source
Destination
B
A
C
D
E
Specifies average rate from source to destination in packets per second

## Slide 39: Example 2: Routing Information
All source-destination flows follow the same route (static routing)
Traffic routed on the direct link (single hop) if possible
If no direct link exists …
  A to/from D routed through B
  A to/from E routed through C
  B to/from E routed through D
There is no re-circulation (no routing loops)

## Slide 40: Example 2: Calculating Throughput
Links are bi-directional, but symmetry ensures capacities are the same in both directions, so let us consider only one direction (“L to R”)
…

## Slide 41: Example 2: Link Table (1)
3.15
3.55
3150
3550
56.12
59.58
6546
7155
0.294
0.277
Pkts/ second
bps
bps1/2
bps
seconds
1:
2:
3:
4:
Link
3.64
3640
60.3
7291
0.274
0.13
130
11.4
820
1.45

## Slide 42: Example 2: Link Table (2)
0.82
3.88
820
3880
28.64
62.29
2553
7649
0.577
0.265
Pkts/ second
bps
bps1/2
bps
seconds
25.12
25120
378.11
48000
0.249
9.95
9950
99.75
15986
0.166
5:
6:
7:
, Avg:
Link

## Slide 43: Min-Max Capacity Assignment
The previous examples (Example 1 and Example 2) minimize average delay, but favor link with high arrival rates
Alternative solution is to minimize the maximum delay … min-max optimization

## Slide 44: Min-Max Solution
Must make delays equal for all links
  Any other allocation raises delay for one or more links
Make the following equal for all i …

## Slide 45: General Min-Max Capacity Assignment
Rule is to assign excess capacity in proportion to mean packet lengths …

## Slide 46: Example 2: Using Min-Max
Repeat Example 2 using min-max assignment
ti (s)
Ci (bps)
Link
1
6,418.6
0.306
2
3
4
5
6
7
6,818.6
3,398.6
6,908.6
4,088.6
7,148.6
13,218.6
0.306
0.306
0.306
0.306
0.306
0.306
Ci (bps)
6,546
7,155
820
7,291
2,553
7,649
15,986
ti (s)
0.294
0.277
1.449
0.274
0.577
0.265
0.166
Total/Avg
48,000
48,000
0.249
?

## Slide 47: Other Cost Functions
Previous cost function was simple
  For example, did not consider distance
More realistic constraint
  Fixed cost per link, ai
  Distance-based or other variable factor per link, di
Dependence on i allows
distance model
Fixed cost

## Slide 48: Available or “Excess” Cost (1)
In previous cases, we looked at “excess capacity”
In an analogous manner, let us define “available cost,” Da …
Results are analogous to those previously derived using excess capacity

## Slide 49: Available or “Excess” Cost (2)
Results: minimum average delay
Results: min-max delay

## Slide 50: Example 3: Star Network, Again
Same topology and load, but use a more complex cost function
  a: fixed cost per link ($)
  B: cost of capacity per mile ($/bps/mile)
q1
q3
q2
C1
C2
C3
HOST

## Slide 51: Example 3: Cost Parameters
Cost
  Variable: B = $0.002 per bit per second per mile
  Fixed: ai = a = $1000 per link
Distances:
  Main: 10 miles
  Branch: 30 miles
  Satellite: 30 miles
Allowed cost: D = $4M

## Slide 52: Example 3: Load Parameters
Packet length: Li = L = 128 bytes
2000 packets per second for each terminal
Number of terminals
  Main: 20
  Branch: 20
  Satellite: 1
 Loading different than in Example 1

## Slide 53: Example 3: Results — Load and Cost
ri
40.96
1:
Link
40.96
2.048
400
2:
3:
S:
Mbps
i
40
40
2
82
KPkts/s
di
0.02
0.06
0.06
—
$/bps

## Slide 54: Example 3: Results — Minimum Average
Ci
E[]
0.8192
50.53
0.107
1:
Link
di ri
2.4576
46.49
0.185
0.1229
3.28
0.828
0.163
3.4000
100.30
2:
3:
S, Avg:
Mbps
ms
M$
905.1
1567.7
350.5
2823.3
$1/2
1.01
2.79
0.20
4.00
M$
Di

## Slide 55: Example 3: Results — Min-Max
Di
E[]
20.48
0.240
0.91
1:
Link
diL
61.44
0.240
2.71
61.44
0.240
0.38
0.240
143.36
4.00
2:
3:
S, Avg:
ms
M$
$•s
45.23
45.23
6.31
96.77
Mbps
Ci

## Slide 56: You should now be able to …
Define the topology design and capacity assignment problems and solution approaches
Analyze cost, capacity, delay, and reliability (k-connectedness) for a network
Apply “excess capacity” and “excess cost” results to determine optimal capacity assignment assuming …
  Minimization of average delay
  Minimization of maximum delay (min-max)